## Slide 2
Version 14.0
File System Enhancements
Richard Smith
21 October 2013

## Slide 3
Versions 10.1, 12.0, 12.1, 13.0, 13.1 and 14.0
File System Enhancements
plus some possibilities for the future
Richard Smith
21 October 2013

## Slide 4: Large Span files
10.1 (2004)
  Large (>4GB) total file size
  Interoperability improvements
  Not default creation mode
  No large individual components

## Slide 5: Large Span files
10.1 (2004)
  Large (>4GB) total file size
  Interoperability improvements
12.0 (2008)
  Default creation mode
  Unicode support
  No large individual components

## Slide 6: Large Span files
10.1 (2004)
  Large (>4GB) total file size
  Interoperability improvements
12.0 (2008)
  Default creation mode
  Unicode support
13.1 (2012)
  Large individual components
[0][1]
Notes: [0] Large Span files = 64 bit files
[1] 13.0 (2011) announced planned withdrawal of small span files

## Slide 7: Journaling
12.0 (2008)
  Journaling level 1
    J0 default creation mode

## Slide 8: Journaling
12.0 (2008)
  Journaling level 1
    J0 default creation mode
12.1 (2009)
  Journaling levels 2 and 3
  Checksumming

## Slide 9: Journaling
12.0 (2008)
  Journaling level 1
    J0 default creation mode
12.1 (2009)
  Journaling levels 2 and 3
  Checksumming
13.1 (2012)
  J1 C1 default creation mode
[2]
Notes: [2] See 2010 Conference paper for more detail

## Slide 10: Data compatibility
Prior to 13.1
  D←⎕FREAD 1 1
  1 + 2
  7
13.1 (2012)
  D←⎕FREAD 1 1
  DOMAIN ERROR: Array is from a later version of APL
[3]
Component contains “unsafe” data from a later release
Notes: [3] “Unsafe” data from later interpreter releases could be read from components (c.f. workspaces); after 13.1 “safe” data can still be read

## Slide 11: Extended Error Reporting
Prior to 13.1
  fid ⎕FTIE 0
  FILE NAME ERROR
13.1 (2012)
  fid ⎕FTIE 0
  FILE NAME ERROR: Unable to open file ("The network path was not found.")

## Slide 12
Version 14.0

## Slide 13: Variant options
Prior to 14.0
  fid ⎕FCREATE 1
  ‘J’ 3 ⎕FPROPS 1
14.0 (2Q 2014)
  fid ⎕FCREATE ⍠ ‘J’ 3 ⊢ 1
  Or fid ⎕FCREATE ⍠ 3 ⊢ 1

## Slide 14: Variant options
14.0 (2Q 2014)
  fid ⎕FTIE ⍠ ‘ReadOnly’ 1 ⊢ 1
  ‘Ducks’ ⎕FAPPEND 1
  FILE ACCESS ERROR: File opened read-only

## Slide 15: Variant options
Prior to 14.0
  ‘REPAIR’ ⎕FCHK fid
14.0 (2Q 2014)
  ⎕FCHK ⍠ ‘Repair’ 1 ⊢ fid
  Or ⎕FCHK ⍠ 1 ⊢ fid
  Or ‘REPAIR’ ⎕FCHK fid

## Slide 16: Small span files
Have restricted functionality
Consume development resources
20 year “phase out”:
  2004: Large span support
  2008: Large span new file default
  2011: Announced withdrawal
  2014: Small span read-only
  … until at least 2024

## Slide 17: Small span files
Prior to 14.0
  fid ⎕FTIE 0
  1
14.0 (2Q 2014)
  fid ⎕FTIE 1
  FILE ACCESS ERROR: Small span files must be tied using the ReadOnly variant option
[4]
Small span file
Notes: [4] Better to give error on tie than write

## Slide 18: Small span files
fid ⎕FTIE ⍠ ‘ReadOnly’ 1 ⊢ 0
  1
  A←⎕FREAD 1
  A ⎕FAPPEND 1
  FILE ACCESS ERROR: File opened read-only

## Slide 19: Converting small span files
‘S’ ⎕FPROPS tie reports span size
⎕FCOPY always creates large span
]FTO64 converts all files in a directory (or directories)
  Supplied with 13.2

## Slide 20: Performance I
Read/write re-implemented in 14.0
No application changes required
Best performance gains with:
  Fast networks
  Congested networks
  Arrays with many elements of mixed type

## Slide 21: Performance II
Prior to 14.0 ⎕FREAD¨1,¨4 6 8
14.0 ⎕FREAD 1 (4 6 8)
  Convenient syntax (perhaps)
  File locked only once
    Semantic difference
    Performance gain

## Slide 22: Performance II
⎕FREAD 1 (4 6 8)
Application changes required
Best performance gains with:
  Share tied files
  (Virtually no gain on exclusive tie)
Huge performance gains with:
  NFS file systems
  (Not bad on others)

## Slide 23: Performance III
‘Z’ ⎕FPROPS 1
  Or fid ⎕FCREATE ⍠ ‘Z’ 1 ⊢ 1
New components are compressed
Decompressed automatically
Compressed components unreadable with 13.2 and earlier
Best performance gains with:
  Slow networks

## Slide 24: Performance analysis
Examples only
Components 1-1000: uncompressed 100 4 matrix (numbers and chars); 12KB each
Components 1001-2000: compressed; 3KB each
Your mileage will vary

## Slide 25: Performance analysis
⎕FREAD¨1,¨⍳1000
⎕FREAD¨1,¨⍳1000
⎕FREAD 1 (⍳1000) ⎕FREAD¨1,¨1000+⍳1000
⎕FREAD 1 (1000+⍳1000)
13.2
14.0
Multiple read
Compress

## Slide 26: Windows; local filesystem
0.16s
0.10s (-37.5%)
0.083s (-48.1%) 0.11s (-31.2%)
0.087s (-45.6%)
13.2
14.0
Multiple read
Compress

## Slide 27: Windows; fast network
0.21s
0.13s (-38.1%)
0.089s (-57.6%) 0.14s (-33.3%)
0.092s (-56.2%)
13.2
14.0
Multiple read
Compress

## Slide 28: Windows; slow network
100s
100s (0%)
100s (0%) 26s (-74%)
25s (-75%)
13.2
14.0
Multiple read
Compress

## Slide 29: Linux; local filesystem
0.17s
0.14s (-17.6%)
0.13s (-23.5%) 0.14s (-17.6%)
0.12s (-29.4%)
13.2
14.0
Multiple read
Compress

## Slide 30: Linux; fast network
3.0s
2.8s (-6.7%)
0.2s (-93.3%) 2.3s (-23.3%)
0.14s (-95.3%)
13.2
14.0
Multiple read
Compress

## Slide 31: AIX; local filesystem
0.23s
0.17s (-26.1%)
0.16s (-30.4%) 0.19s (-17.3%)
0.18s (-21.7%)
13.2
14.0
Multiple read
Compress

## Slide 32: AIX; fast network
4.4s
2.3s (-47.7%)
0.89s (-79.8%) 2.1s (-52.3%)
0.66s (-85%)
[5]
13.2
14.0
Multiple read
Compress
Notes: Real world example: 50s → 5s

## Slide 34: Possibilities for the future
Performance improvements
  Multi-tie ⎕FREAD.
  Multi-component/tie ⎕FWRITE, ⎕FAPPEND.
  Async. read/write.
Encryption.
All files journaled and checksummed.
Transactions

## Slide 35: Transactions
⎕FHOLD t1 t2 a←⎕FREAD t1 (⊃⎕FSIZE t1) a ⎕FAPPEND t2 ⎕FDROP t1 1 ⎕FHOLD ⍬

## Slide 36: Transactions
⎕FHOLD ⍠ ‘Txn’ ‘Begin’ ⊢ t1 t2 a←⎕FREAD t1 (⊃⎕FSIZE t1) a ⎕FAPPEND t2 ⎕FDROP t1 1 ⎕FHOLD ⍠ ‘Txn’ ‘Commit’ ⊢ ⍬

## Slide 37: Transactions
:TRAP 0 ⎕FHOLD ⍠ ‘Txn’ ‘Begin’ ⊢ t1 t2 a←⎕FREAD t1 (⊃⎕FSIZE t1) a ⎕FAPPEND t2 ⎕FDROP t1 1 ⎕FHOLD ⍠ ‘Txn’ ‘Commit’ ⊢ ⍬ :ELSE ⎕FHOLD ⍠ ‘Txn’ ‘Rollback’ ⊢ ⍬ :ENDTRAP

## Slide 38: Summary
Large/small span files
Journaling and checksumming
Data compatibility checks
Extended error reporting
Variant support
Performance improvements
Encryption
Transactions

## Slide 39
Version 14.0 et al
File System Enhancements
Richard Smith
21 October 2013
Notes: Question time