## Slide 1: Grain Growth and Array Programming
jgl@dyalog.com
jesus.galanlopez@ugent.be

## Slide 2
Based on a true story

## Slide 3: Problem statement

## Slide 4: Problem statement
Materials science students

## Slide 5: Problem statement
Materials science students
Choose modelling problem

## Slide 6: Problem statement
Materials science students
Choose modelling problem
Scientific literature

## Slide 7: Problem statement
Materials science students
Choose modelling problem
Scientific literature
Reproduce model

## Slide 8: Grain Growth
Increment of size of grains in a polycrystal subjected to high temperatures
Dimokrati, A., & Benyoucef, M. (2016, September)
Phase Field Simulation of Normal Grain Growth
CONAT 2016

## Slide 9: Grain Growth (Geiger, 2001)
https://doi.org/10.1016/S1359-6454(00)00352-9

## Slide 10: Grain Growth (Geiger, 2001)
Thermal energy
Boundary energy
Activation energy
https://doi.org/10.1016/S1359-6454(00)00352-9

## Slide 11: Grain Growth (Geiger, 2001)
https://doi.org/10.1016/S1359-6454(00)00352-9
Maxwell-Boltzmann distribution
Thermal energy
Boundary energy
Activation energy

## Slide 12: Grain Growth (Geiger, 2001)
Thermal energy
Boundary energy
Activation energy
https://doi.org/10.1016/S1359-6454(00)00352-9
Read-Shockley equation
Misorientation

## Slide 13: Grain Growth (Geiger, 2001)
Thermal energy
Boundary energy
Activation energy
https://doi.org/10.1016/S1359-6454(00)00352-9

## Slide 14: Grain Growth (Geiger, 2001)
Thermal energy
Boundary energy
Activation energy
https://doi.org/10.1016/S1359-6454(00)00352-9
Geiger, J., Roósz, A., & Barkoczy, P. (2001). Simulation of grain coarsening in two dimensions by cellular-automaton. Acta materialia, 49(4), 623-629.
Transform into neighbour with minimum new boundary energy
G1
G2
GA
GT
G12

## Slide 15: Grain Growth (Geiger, 2001)
https://doi.org/10.1016/S1359-6454(00)00352-9
Geiger, J., Roósz, A., & Barkoczy, P. (2001). Simulation of grain coarsening in two dimensions by cellular-automaton. Acta materialia, 49(4), 623-629.
Transform into neighbour with minimum new boundary energy
Thermal energy
Boundary energy
Activation energy
G1
G2
GA
GT
G12

## Slide 16: First solution

## Slide 17: First solution (Python)
The students know some Python
Python is easy!
Python is there

## Slide 18: First solution (Python)
import numpy as np
import matplotlib.pyplot as plt
from skimage.measure import regionprops
from skimage.morphology import label
from timeit import timeit
R = 8.314 # ideal gas constant
GA = 10000 # activation energy
G0 = 3000 # maximum boundary energy
# thermal energy according to Maxwell-Boltzmann distribution at temperature T (kelvin)
def thermal(T):
return -R*T*np.log(1-np.random.random())
# misorientation angle (in radians) between q and q1
def misorientation(q, q1, qmax):
return (np.pi/2)*np.abs(q-q1)/qmax
# total boundary energy of cell with orientation q and neighbours with orientations q1
def cell_boundary(q, q1, qmax):
gb = 0
for qi in q1:
dg = misorientation(q, qi, qmax)
sin = np.sin(dg)
if sin > 0:
gb += G0*sin*(1-np.log(sin)) if sin > 0 else 0 # Read-Shockley equation
return gb
def solve(q, T, f=0, n=0):
i, d = 0, []
qmax = np.max(q)
while True:
di = diameter(q)
d.append(di)
if f > 0 and i%f == 0:
plot(q, qmax, "%d (%.2f)"%(i,di))
i, (q, changed) = i+1, step(q, qmax, T)
if (not changed and n == 0) or i == n:
break
# final microstructure
if f > 0:
plot(q, qmax, "%d (%.2f)"%(i,diameter(q)))
return q, d
# return next orientation map q, after grain growth step at temperature T,
# and a boolean indicating if there was any change
def step(q, qmax, T):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[i-1 if i>0 else nr-1,j]
s = q[i+1 if i<nr-1 else 0,j]
e = q[i,j+1 if j<nc-1 else 0]
w = q[i,j-1 if j>0 else nc-1]
q1 = [n, s, e, w]
# check if a cell will transform into some neighbour
if (q1.count(q[i,j]) == len(q1)) or (thermal(T) + cell_boundary(q[i,j], q1, qmax) < GA):
continue
# calculate new boundary energy when transforming into each neighbour
gbn = cell_boundary(n, q1, qmax)
gbs = cell_boundary(s, q1, qmax)
gbe = cell_boundary(e, q1, qmax)
gbw = cell_boundary(w, q1, qmax)
gb1 = [gbn, gbs, gbe, gbw]
# pick product for which the boundary energy is the lowest
p[i,j] = q1[np.argmin(gb1)]
# check if the orientation changed
if p[i,j] != q[i,j]:
changed = True
return p, changed

## Slide 19: First solution (Python)
# return next orientation map q, after grain growth step at temperature T,
# and a boolean indicating if there was any change
def step(q, qmax, T):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[i-1 if i>0 else nr-1,j]
s = q[i+1 if i<nr-1 else 0,j]
e = q[i,j+1 if j<nc-1 else 0]
w = q[i,j-1 if j>0 else nc-1]
q1 = [n, s, e, w]
# check if a cell will transform into some neighbour
if (q1.count(q[i,j]) == len(q1)) or (thermal(T) + cell_boundary(q[i,j], q1, qmax) < GA):
continue
# calculate new boundary energy when transforming into each neighbour
gbn = cell_boundary(n, q1, qmax)
gbs = cell_boundary(s, q1, qmax)
gbe = cell_boundary(e, q1, qmax)
gbw = cell_boundary(w, q1, qmax)
gb1 = [gbn, gbs, gbe, gbw]
# pick product for which the boundary energy is the lowest
p[i,j] = q1[np.argmin(gb1)]
# check if the orientation changed
if p[i,j] != q[i,j]:
changed = True
return p, changed

## Slide 20: First solution (Python)
# return next orientation map q, after grain growth step at temperature T,
# and a boolean indicating if there was any change
def step(q, qmax, T):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[i-1 if i>0 else nr-1,j]
s = q[i+1 if i<nr-1 else 0,j]
e = q[i,j+1 if j<nc-1 else 0]
w = q[i,j-1 if j>0 else nc-1]
q1 = [n, s, e, w]
# check if a cell will transform into some neighbour
if (q1.count(q[i,j]) == len(q1)) or (thermal(T) + cell_boundary(q[i,j], q1, qmax) < GA):
continue
# calculate new boundary energy when transforming into each neighbour
gbn = cell_boundary(n, q1, qmax)
gbs = cell_boundary(s, q1, qmax)
gbe = cell_boundary(e, q1, qmax)
gbw = cell_boundary(w, q1, qmax)
gb1 = [gbn, gbs, gbe, gbw]
# pick product for which the boundary energy is the lowest
p[i,j] = q1[np.argmin(gb1)]
# check if the orientation changed
if p[i,j] != q[i,j]:
changed = True
return p, changed
Loops

## Slide 21: First solution (Python)
Average
Grain Diameter
Random microstructure

## Slide 22: First solution (Python)
Circle Diameter
Single circular grain

## Slide 23: First solution (Python)
# return next orientation map q, after grain growth step at temperature T,
# and a boolean indicating if there was any change
def step(q, qmax, T):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[i-1 if i>0 else nr-1,j]
s = q[i+1 if i<nr-1 else 0,j]
e = q[i,j+1 if j<nc-1 else 0]
w = q[i,j-1 if j>0 else nc-1]
q1 = [n, s, e, w]
# check if a cell will transform into some neighbour
if (q1.count(q[i,j]) == len(q1)) or (thermal(T) + cell_boundary(q[i,j], q1, qmax) < GA):
continue
# calculate new boundary energy when transforming into each neighbour
gbn = cell_boundary(n, q1, qmax)
gbs = cell_boundary(s, q1, qmax)
gbe = cell_boundary(e, q1, qmax)
gbw = cell_boundary(w, q1, qmax)
gb1 = [gbn, gbs, gbe, gbw]
# pick product for which the boundary energy is the lowest
p[i,j] = q1[np.argmin(gb1)]
# check if the orientation changed
if p[i,j] != q[i,j]:
changed = True
return p, changed

## Slide 24: First solution (Python)
# return next orientation map q, after grain growth step at temperature T,
# and a boolean indicating if there was any change
def step(q, qmax, T):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[i-1 if i>0 else nr-1,j]
s = q[i+1 if i<nr-1 else 0,j]
e = q[i,j+1 if j<nc-1 else 0]
w = q[i,j-1 if j>0 else nc-1]
q1 = [n, s, e, w]
# check if a cell will transform into some neighbour
if (q1.count(q[i,j]) == len(q1)) or (thermal(T) + cell_boundary(q[i,j], q1, qmax) < GA):
continue
# calculate new boundary energy when transforming into each neighbour
gbn = cell_boundary(n, q1, qmax)
gbs = cell_boundary(s, q1, qmax)
gbe = cell_boundary(e, q1, qmax)
gbw = cell_boundary(w, q1, qmax)
gb1 = [gbn, gbs, gbe, gbw]
# pick product for which the boundary energy is the lowest
p[i,j] = q1[np.argmin(gb1)]
# check if the orientation changed
if p[i,j] != q[i,j]:
changed = True
return p, changed
?

## Slide 25: Partial Results
Thermal energy
Current boundary energy
Boundary energy when transforming into each neighbour
New orientations (transformed cells)

## Slide 26: First solution (Python)
# return next orientation map q, after grain growth step at temperature T,
# and a boolean indicating if there was any change
def step(q, qmax, T):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[i-1 if i>0 else nr-1,j]
s = q[i+1 if i<nr-1 else 0,j]
e = q[i,j+1 if j<nc-1 else 0]
w = q[i,j-1 if j>0 else nc-1]
q1 = [n, s, e, w]
# check if a cell will transform into some neighbour
if (q1.count(q[i,j]) == len(q1)) or (thermal(T) + cell_boundary(q[i,j], q1, qmax) < GA):
continue
# calculate new boundary energy when transforming into each neighbour
gbn = cell_boundary(n, q1, qmax)
gbs = cell_boundary(s, q1, qmax)
gbe = cell_boundary(e, q1, qmax)
gbw = cell_boundary(w, q1, qmax)
gb1 = [gbn, gbs, gbe, gbw]
# pick product for which the boundary energy is the lowest
p[i,j] = q1[np.argmin(gb1)]
# check if the orientation changed
if p[i,j] != q[i,j]:
changed = True
return p, changed

## Slide 27: Partial Results (Python)
# new version of step that plots partial results if plt is True
def step_partial(q, qmax, T, plt):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
gt = np.zeros(q.shape) # thermal energy
gb = np.zeros(q.shape) # current grain boundary energy
gbn = np.zeros(q.shape) # new grain boundary energy if transforms into north neighbour
gbs = np.zeros(q.shape) # new grain boundary energy if transforms into south neighbour
gbe = np.zeros(q.shape) # new grain boundary energy if transforms into east neighbour
gbw = np.zeros(q.shape) # new grain boundary energy if transforms into west neighbour
m = np.zeros(q.shape, dtype=int) # neighbour for which new grain boundary energy is minimum
t = np.zeros(q.shape, dtype=bool) # cells that will transform
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[(i-1 if i>0 else nr-1),j]
s = q[(i+1 if i<nr-1 else 0),j]
e = q[i,(j+1 if j<nc-1 else 0)]
w = q[i,(j-1 if j>0 else nc-1)]
q1 = [n, s, e, w]
# calculate current boundary energy
gb[i,j] = cell_boundary(q[i,j], q1, qmax)
# and when transforming into each neighbour
gbn[i,j] = cell_boundary(n, q1, qmax)
gbs[i,j] = cell_boundary(s, q1, qmax)
gbe[i,j] = cell_boundary(e, q1, qmax)
gbw[i,j] = cell_boundary(w, q1, qmax)
gb1 = [gbn[i,j], gbs[i,j], gbe[i,j], gbw[i,j]]
# find neighbour for which new boundary energy is minimum
m[i,j] = np.argmin(gb1)
# thermal energy
gt[i,j] = thermal(T)
# check if a cell will transform into some neighbour
t[i,j] = (q1.count(q[i,j]) != len(q1)) and (gt[i,j] + gb[i,j] >= GA)
if not t[i,j]:
continue
# pick orientation of neighbour with minimum new boundary energy
p[i,j] = q1[m[i,j]]
# check if the cell changed of orientation
if p[i,j] != q[i,j]:
changed = True
if plt:
plot_partial(gt, gb, [gbn, gbs, gbe, gbw], m, t)
return p, changed

## Slide 28: Partial Results (Python)
Define arrays
Fill arrays inside loop
# new version of step that plots partial results if plt is True
def step_partial(q, qmax, T, plt):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
gt = np.zeros(q.shape) # thermal energy
gb = np.zeros(q.shape) # current grain boundary energy
gbn = np.zeros(q.shape) # new grain boundary energy if transforms into north neighbour
gbs = np.zeros(q.shape) # new grain boundary energy if transforms into south neighbour
gbe = np.zeros(q.shape) # new grain boundary energy if transforms into east neighbour
gbw = np.zeros(q.shape) # new grain boundary energy if transforms into west neighbour
m = np.zeros(q.shape, dtype=int) # neighbour for which new grain boundary energy is minimum
t = np.zeros(q.shape, dtype=bool) # cells that will transform
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[(i-1 if i>0 else nr-1),j]
s = q[(i+1 if i<nr-1 else 0),j]
e = q[i,(j+1 if j<nc-1 else 0)]
w = q[i,(j-1 if j>0 else nc-1)]
q1 = [n, s, e, w]
# calculate current boundary energy
gb[i,j] = cell_boundary(q[i,j], q1, qmax)
# and when transforming into each neighbour
gbn[i,j] = cell_boundary(n, q1, qmax)
gbs[i,j] = cell_boundary(s, q1, qmax)
gbe[i,j] = cell_boundary(e, q1, qmax)
gbw[i,j] = cell_boundary(w, q1, qmax)
gb1 = [gbn[i,j], gbs[i,j], gbe[i,j], gbw[i,j]]
# find neighbour for which new boundary energy is minimum
m[i,j] = np.argmin(gb1)
# thermal energy
gt[i,j] = thermal(T)
# check if a cell will transform into some neighbour
t[i,j] = (q1.count(q[i,j]) != len(q1)) and (gt[i,j] + gb[i,j] >= GA)
if not t[i,j]:
continue
# pick orientation of neighbour with minimum new boundary energy
p[i,j] = q1[m[i,j]]
# check if the cell changed of orientation
if p[i,j] != q[i,j]:
changed = True
if plt:
plot_partial(gt, gb, [gbn, gbs, gbe, gbw], m, t)
return p, changed

## Slide 29: Partial Results (Python)
New boundary energy
Same change of energy for all neighbours

## Slide 30: Partial Results (Python)
Cells transform only into north and south neighbours

## Slide 31: Partial Results (Python)
Cells transform only into north and south neighbours
Randomize choice of neighbour with minimum energy

## Slide 32: Partial Results (Python)
# new version of step that plots partial results if plt is True
def step_partial(q, qmax, T, plt):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
gt = np.zeros(q.shape) # thermal energy
gb = np.zeros(q.shape) # current grain boundary energy
gbn = np.zeros(q.shape) # new grain boundary energy if transforms into north neighbour
gbs = np.zeros(q.shape) # new grain boundary energy if transforms into south neighbour
gbe = np.zeros(q.shape) # new grain boundary energy if transforms into east neighbour
gbw = np.zeros(q.shape) # new grain boundary energy if transforms into west neighbour
m = np.zeros(q.shape, dtype=int) # neighbour for which new grain boundary energy is minimum
t = np.zeros(q.shape, dtype=bool) # cells that will transform
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[(i-1 if i>0 else nr-1),j]
s = q[(i+1 if i<nr-1 else 0),j]
e = q[i,(j+1 if j<nc-1 else 0)]
w = q[i,(j-1 if j>0 else nc-1)]
q1 = [n, s, e, w]
# calculate current boundary energy
gb[i,j] = cell_boundary(q[i,j], q1, qmax)
# and when transforming into each neighbour
gbn[i,j] = cell_boundary(n, q1, qmax)
gbs[i,j] = cell_boundary(s, q1, qmax)
gbe[i,j] = cell_boundary(e, q1, qmax)
gbw[i,j] = cell_boundary(w, q1, qmax)
gb1 = [gbn[i,j], gbs[i,j], gbe[i,j], gbw[i,j]]
# find neighbour for which new boundary energy is minimum
m[i,j] = np.argmin(gb1)
# thermal energy
gt[i,j] = thermal(T)
# check if a cell will transform into some neighbour
t[i,j] = (q1.count(q[i,j]) != len(q1)) and (gt[i,j] + gb[i,j] >= GA)
if not t[i,j]:
continue
# pick orientation of neighbour with minimum new boundary energy
p[i,j] = q1[m[i,j]]
# check if the cell changed of orientation
if p[i,j] != q[i,j]:
changed = True
if plt:
plot_partial(gt, gb, [gbn, gbs, gbe, gbw], m, t)
return p, changed

## Slide 33: Random Perturbation (Python)
# new version of step_partial which applies a random perturbation to
# new boundary energies before searching the minimum
def step_rnd(q, qmax, T, plt):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
gt = np.zeros(q.shape) # thermal energy
gb = np.zeros(q.shape) # current grain boundary energy
gbn = np.zeros(q.shape) # new grain boundary energy if transforms into north neighbour
gbs = np.zeros(q.shape) # new grain boundary energy if transforms into south neighbour
gbe = np.zeros(q.shape) # new grain boundary energy if transforms into east neighbour
gbw = np.zeros(q.shape) # new grain boundary energy if transforms into west neighbour
m = np.zeros(q.shape, dtype=int) # neighbour for which new grain boundary energy is minimum
t = np.zeros(q.shape, dtype=bool) # cells that will transform
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[(i-1 if i>0 else nr-1),j]
s = q[(i+1 if i<nr-1 else 0),j]
e = q[i,(j+1 if j<nc-1 else 0)]
w = q[i,(j-1 if j>0 else nc-1)]
q1 = [n, s, e, w]
# calculate current boundary energy
gb[i,j] = cell_boundary(q[i,j], q1, qmax)
# and when transforming into each neighbour
gbn[i,j] = cell_boundary(n, q1, qmax) * (1 + RP * np.random.random())
gbs[i,j] = cell_boundary(s, q1, qmax) * (1 + RP * np.random.random())
gbe[i,j] = cell_boundary(e, q1, qmax) * (1 + RP * np.random.random())
gbw[i,j] = cell_boundary(w, q1, qmax) * (1 + RP * np.random.random())
gb1 = [gbn[i,j], gbs[i,j], gbe[i,j], gbw[i,j]]
# find neighbour for which new boundary energy is minimum
m[i,j] = np.argmin(gb1)
# thermal energy
gt[i,j] = thermal(T)
# check if a cell will transform into some neighbour
t[i,j] = (q1.count(q[i,j]) != len(q1)) and (gt[i,j] + gb[i,j] >= GA)
if not t[i,j]:
continue
# pick orientation of neighbour with minimum new boundary energy
p[i,j] = q1[m[i,j]]
# check if the cell changed of orientation
if p[i,j] != q[i,j]:
changed = True
if plt:
plot_partial(gt, gb, [gbn, gbs, gbe, gbw], m, t)
return p, changed
RP = 0.01 # random perturbation

## Slide 34: Random Perturbation (Python)
Apply small random perturbation to new boundary energies
RP = 0.01 # random perturbation
# new version of step_partial which applies a random perturbation to
# new boundary energies before searching the minimum
def step_rnd(q, qmax, T, plt):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
gt = np.zeros(q.shape) # thermal energy
gb = np.zeros(q.shape) # current grain boundary energy
gbn = np.zeros(q.shape) # new grain boundary energy if transforms into north neighbour
gbs = np.zeros(q.shape) # new grain boundary energy if transforms into south neighbour
gbe = np.zeros(q.shape) # new grain boundary energy if transforms into east neighbour
gbw = np.zeros(q.shape) # new grain boundary energy if transforms into west neighbour
m = np.zeros(q.shape, dtype=int) # neighbour for which new grain boundary energy is minimum
t = np.zeros(q.shape, dtype=bool) # cells that will transform
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[(i-1 if i>0 else nr-1),j]
s = q[(i+1 if i<nr-1 else 0),j]
e = q[i,(j+1 if j<nc-1 else 0)]
w = q[i,(j-1 if j>0 else nc-1)]
q1 = [n, s, e, w]
# calculate current boundary energy
gb[i,j] = cell_boundary(q[i,j], q1, qmax)
# and when transforming into each neighbour
gbn[i,j] = cell_boundary(n, q1, qmax) * (1 + RP * np.random.random())
gbs[i,j] = cell_boundary(s, q1, qmax) * (1 + RP * np.random.random())
gbe[i,j] = cell_boundary(e, q1, qmax) * (1 + RP * np.random.random())
gbw[i,j] = cell_boundary(w, q1, qmax) * (1 + RP * np.random.random())
gb1 = [gbn[i,j], gbs[i,j], gbe[i,j], gbw[i,j]]
# find neighbour for which new boundary energy is minimum
m[i,j] = np.argmin(gb1)
# thermal energy
gt[i,j] = thermal(T)
# check if a cell will transform into some neighbour
t[i,j] = (q1.count(q[i,j]) != len(q1)) and (gt[i,j] + gb[i,j] >= GA)
if not t[i,j]:
continue
# pick orientation of neighbour with minimum new boundary energy
p[i,j] = q1[m[i,j]]
# check if the cell changed of orientation
if p[i,j] != q[i,j]:
changed = True
if plt:
plot_partial(gt, gb, [gbn, gbs, gbe, gbw], m, t)
return p, changed

## Slide 35: Random Perturbation (Python)
Neighbour into which to transform is randomly chosen

## Slide 36: Random Perturbation
Circle Diameter
Single circular grain

## Slide 37: Other problems
Unrealistic “checkboard pattern”

## Slide 38: Other problems
Unrealistic “checkboard pattern”
Consider second order neighbours

## Slide 39: Random Perturbation (Python)
# new version of step_partial which applies a random perturbation to
# new boundary energies before searching the minimum
def step_rnd(q, qmax, T, plt):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
gt = np.zeros(q.shape) # thermal energy
gb = np.zeros(q.shape) # current grain boundary energy
gbn = np.zeros(q.shape) # new grain boundary energy if transforms into north neighbour
gbs = np.zeros(q.shape) # new grain boundary energy if transforms into south neighbour
gbe = np.zeros(q.shape) # new grain boundary energy if transforms into east neighbour
gbw = np.zeros(q.shape) # new grain boundary energy if transforms into west neighbour
m = np.zeros(q.shape, dtype=int) # neighbour for which new grain boundary energy is minimum
t = np.zeros(q.shape, dtype=bool) # cells that will transform
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[(i-1 if i>0 else nr-1),j]
s = q[(i+1 if i<nr-1 else 0),j]
e = q[i,(j+1 if j<nc-1 else 0)]
w = q[i,(j-1 if j>0 else nc-1)]
q1 = [n, s, e, w]
# calculate current boundary energy
gb[i,j] = cell_boundary(q[i,j], q1, qmax)
# and when transforming into each neighbour
gbn[i,j] = cell_boundary(n, q1, qmax) * (1 + RP * np.random.random())
gbs[i,j] = cell_boundary(s, q1, qmax) * (1 + RP * np.random.random())
gbe[i,j] = cell_boundary(e, q1, qmax) * (1 + RP * np.random.random())
gbw[i,j] = cell_boundary(w, q1, qmax) * (1 + RP * np.random.random())
gb1 = [gbn[i,j], gbs[i,j], gbe[i,j], gbw[i,j]]
# find neighbour for which new boundary energy is minimum
m[i,j] = np.argmin(gb1)
# thermal energy
gt[i,j] = thermal(T)
# check if a cell will transform into some neighbour
t[i,j] = (q1.count(q[i,j]) != len(q1)) and (gt[i,j] + gb[i,j] >= GA)
if not t[i,j]:
continue
# pick orientation of neighbour with minimum new boundary energy
p[i,j] = q1[m[i,j]]
# check if the cell changed of orientation
if p[i,j] != q[i,j]:
changed = True
if plt:
plot_partial(gt, gb, [gbn, gbs, gbe, gbw], m, t)
return p, changed
RP = 0.01 # random perturbation

## Slide 40: 2nd order neighbours (Python)
# new version of step_rnd which takes into account the influence of secon-order neighbours
def step_rnd2(q, qmax, T, plt):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
gt = np.zeros(q.shape) # thermal energy
gb = np.zeros(q.shape) # current grain boundary energy
gbn = np.zeros(q.shape) # new grain boundary energy if transforms into north neighbour
gbs = np.zeros(q.shape) # new grain boundary energy if transforms into south neighbour
gbe = np.zeros(q.shape) # new grain boundary energy if transforms into east neighbour
gbw = np.zeros(q.shape) # new grain boundary energy if transforms into west neighbour
m = np.zeros(q.shape, dtype=int) # neighbour for which new grain boundary energy is minimum
t = np.zeros(q.shape, dtype=bool) # cells that will transform
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[(i-1 if i>0 else nr-1),j]
s = q[(i+1 if i<nr-1 else 0),j]
e = q[i,(j+1 if j<nc-1 else 0)]
w = q[i,(j-1 if j>0 else nc-1)]
q1 = [n, s, e, w]
# calculate current boundary energy
gb[i,j] = cell_boundary(q[i,j], q1, qmax)
# and when transforming into each neighbour
gbn[i,j] = cell_boundary(n, q1, qmax)
gbs[i,j] = cell_boundary(s, q1, qmax)
gbe[i,j] = cell_boundary(e, q1, qmax)
gbw[i,j] = cell_boundary(w, q1, qmax)
if SF > 0:
nw = q[(i-1 if i>0 else nr-1),(j-1 if j>0 else nc-1)]
se = q[(i+1 if i<nr-1 else 0),(j+1 if j<nc-1 else 0)]
ne = q[(i-1 if i>0 else nr-1),(j+1 if j<nc-1 else 0)]
sw = q[(i+1 if i<nr-1 else 0),(j-1 if j>0 else nc-1)]
q2 = [nw, se, ne, sw]
gbn[i,j] += SF * cell_boundary(n, q2, qmax)
gbs[i,j] += SF * cell_boundary(s, q2, qmax)
gbe[i,j] += SF * cell_boundary(e, q2, qmax)
gbw[i,j] += SF * cell_boundary(w, q2, qmax)
gbn[i,j] *= 1 + RP * np.random.random()
gbs[i,j] *= 1 + RP * np.random.random()
gbe[i,j] *= 1 + RP * np.random.random()
gbw[i,j] *= 1 + RP * np.random.random()
gb1 = [gbn[i,j], gbs[i,j], gbe[i,j], gbw[i,j]]
# find neighbour for which new boundary energy is minimum
m[i,j] = np.argmin(gb1)
# thermal energy
gt[i,j] = thermal(T)
# check if a cell will transform into some neighbour
t[i,j] = (q1.count(q[i,j]) != len(q1)) and (gt[i,j] + gb[i,j] >= GA)
if not t[i,j]:
continue
# pick orientation of neighbour with minimum new boundary energy
p[i,j] = q1[m[i,j]]
# check if the cell changed of orientation
if p[i,j] != q[i,j]:
changed = True
if plt:
plot_partial(gt, gb, [gbn, gbs, gbe, gbw], 'NSEW', m, t)
return p, changed
RP = 0.01 # random perturbation
SF = 0.25 # second-order-neighbours factor

## Slide 41: 2nd order
Circle Diameter
Average Diameter

## Slide 42: 2nd order neighbours (Python)
# new version of step_rnd which takes into account the influence of secon-order neighbours
def step_rnd2(q, qmax, T, plt):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
gt = np.zeros(q.shape) # thermal energy
gb = np.zeros(q.shape) # current grain boundary energy
gbn = np.zeros(q.shape) # new grain boundary energy if transforms into north neighbour
gbs = np.zeros(q.shape) # new grain boundary energy if transforms into south neighbour
gbe = np.zeros(q.shape) # new grain boundary energy if transforms into east neighbour
gbw = np.zeros(q.shape) # new grain boundary energy if transforms into west neighbour
m = np.zeros(q.shape, dtype=int) # neighbour for which new grain boundary energy is minimum
t = np.zeros(q.shape, dtype=bool) # cells that will transform
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[(i-1 if i>0 else nr-1),j]
s = q[(i+1 if i<nr-1 else 0),j]
e = q[i,(j+1 if j<nc-1 else 0)]
w = q[i,(j-1 if j>0 else nc-1)]
q1 = [n, s, e, w]
# calculate current boundary energy
gb[i,j] = cell_boundary(q[i,j], q1, qmax)
# and when transforming into each neighbour
gbn[i,j] = cell_boundary(n, q1, qmax)
gbs[i,j] = cell_boundary(s, q1, qmax)
gbe[i,j] = cell_boundary(e, q1, qmax)
gbw[i,j] = cell_boundary(w, q1, qmax)
if SF > 0:
nw = q[(i-1 if i>0 else nr-1),(j-1 if j>0 else nc-1)]
se = q[(i+1 if i<nr-1 else 0),(j+1 if j<nc-1 else 0)]
ne = q[(i-1 if i>0 else nr-1),(j+1 if j<nc-1 else 0)]
sw = q[(i+1 if i<nr-1 else 0),(j-1 if j>0 else nc-1)]
q2 = [nw, se, ne, sw]
gbn[i,j] += SF * cell_boundary(n, q2, qmax)
gbs[i,j] += SF * cell_boundary(s, q2, qmax)
gbe[i,j] += SF * cell_boundary(e, q2, qmax)
gbw[i,j] += SF * cell_boundary(w, q2, qmax)
gbn[i,j] *= 1 + RP * np.random.random()
gbs[i,j] *= 1 + RP * np.random.random()
gbe[i,j] *= 1 + RP * np.random.random()
gbw[i,j] *= 1 + RP * np.random.random()
gb1 = [gbn[i,j], gbs[i,j], gbe[i,j], gbw[i,j]]
# find neighbour for which new boundary energy is minimum
m[i,j] = np.argmin(gb1)
# thermal energy
gt[i,j] = thermal(T)
# check if a cell will transform into some neighbour
t[i,j] = (q1.count(q[i,j]) != len(q1)) and (gt[i,j] + gb[i,j] >= GA)
if not t[i,j]:
continue
# pick orientation of neighbour with minimum new boundary energy
p[i,j] = q1[m[i,j]]
# check if the cell changed of orientation
if p[i,j] != q[i,j]:
changed = True
if plt:
plot_partial(gt, gb, [gbn, gbs, gbe, gbw], 'NSEW', m, t)
return p, changed
RP = 0.01 # random perturbation
SF = 0.25 # second-order-neighbours factor

## Slide 43: 2nd order neighbours (Python)
# new version of step_rnd which takes into account the influence of secon-order neighbours
def step_rnd2(q, qmax, T, plt):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
gt = np.zeros(q.shape) # thermal energy
gb = np.zeros(q.shape) # current grain boundary energy
gbn = np.zeros(q.shape) # new grain boundary energy if transforms into north neighbour
gbs = np.zeros(q.shape) # new grain boundary energy if transforms into south neighbour
gbe = np.zeros(q.shape) # new grain boundary energy if transforms into east neighbour
gbw = np.zeros(q.shape) # new grain boundary energy if transforms into west neighbour
m = np.zeros(q.shape, dtype=int) # neighbour for which new grain boundary energy is minimum
t = np.zeros(q.shape, dtype=bool) # cells that will transform
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[(i-1 if i>0 else nr-1),j]
s = q[(i+1 if i<nr-1 else 0),j]
e = q[i,(j+1 if j<nc-1 else 0)]
w = q[i,(j-1 if j>0 else nc-1)]
q1 = [n, s, e, w]
# calculate current boundary energy
gb[i,j] = cell_boundary(q[i,j], q1, qmax)
# and when transforming into each neighbour
gbn[i,j] = cell_boundary(n, q1, qmax)
gbs[i,j] = cell_boundary(s, q1, qmax)
gbe[i,j] = cell_boundary(e, q1, qmax)
gbw[i,j] = cell_boundary(w, q1, qmax)
if SF > 0:
nw = q[(i-1 if i>0 else nr-1),(j-1 if j>0 else nc-1)]
se = q[(i+1 if i<nr-1 else 0),(j+1 if j<nc-1 else 0)]
ne = q[(i-1 if i>0 else nr-1),(j+1 if j<nc-1 else 0)]
sw = q[(i+1 if i<nr-1 else 0),(j-1 if j>0 else nc-1)]
q2 = [nw, se, ne, sw]
gbn[i,j] += SF * cell_boundary(n, q2, qmax)
gbs[i,j] += SF * cell_boundary(s, q2, qmax)
gbe[i,j] += SF * cell_boundary(e, q2, qmax)
gbw[i,j] += SF * cell_boundary(w, q2, qmax)
gbn[i,j] *= 1 + RP * np.random.random()
gbs[i,j] *= 1 + RP * np.random.random()
gbe[i,j] *= 1 + RP * np.random.random()
gbw[i,j] *= 1 + RP * np.random.random()
gb1 = [gbn[i,j], gbs[i,j], gbe[i,j], gbw[i,j]]
# find neighbour for which new boundary energy is minimum
m[i,j] = np.argmin(gb1)
# thermal energy
gt[i,j] = thermal(T)
# check if a cell will transform into some neighbour
t[i,j] = (q1.count(q[i,j]) != len(q1)) and (gt[i,j] + gb[i,j] >= GA)
if not t[i,j]:
continue
# pick orientation of neighbour with minimum new boundary energy
p[i,j] = q1[m[i,j]]
# check if the cell changed of orientation
if p[i,j] != q[i,j]:
changed = True
if plt:
plot_partial(gt, gb, [gbn, gbs, gbe, gbw], 'NSEW', m, t)
return p, changed
Too much repetitive code
Hard to understand what the model is doing
Easy to make mistakes
Slow
RP = 0.01 # random perturbation
SF = 0.25 # second-order-neighbours factor

## Slide 44: 2nd order neighbours (Python)
# new version of step_rnd which takes into account the influence of secon-order neighbours
def step_rnd2(q, qmax, T, plt):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
gt = np.zeros(q.shape) # thermal energy
gb = np.zeros(q.shape) # current grain boundary energy
gbn = np.zeros(q.shape) # new grain boundary energy if transforms into north neighbour
gbs = np.zeros(q.shape) # new grain boundary energy if transforms into south neighbour
gbe = np.zeros(q.shape) # new grain boundary energy if transforms into east neighbour
gbw = np.zeros(q.shape) # new grain boundary energy if transforms into west neighbour
m = np.zeros(q.shape, dtype=int) # neighbour for which new grain boundary energy is minimum
t = np.zeros(q.shape, dtype=bool) # cells that will transform
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[(i-1 if i>0 else nr-1),j]
s = q[(i+1 if i<nr-1 else 0),j]
e = q[i,(j+1 if j<nc-1 else 0)]
w = q[i,(j-1 if j>0 else nc-1)]
q1 = [n, s, e, w]
# calculate current boundary energy
gb[i,j] = cell_boundary(q[i,j], q1, qmax)
# and when transforming into each neighbour
gbn[i,j] = cell_boundary(n, q1, qmax)
gbs[i,j] = cell_boundary(s, q1, qmax)
gbe[i,j] = cell_boundary(e, q1, qmax)
gbw[i,j] = cell_boundary(w, q1, qmax)
if SF > 0:
nw = q[(i-1 if i>0 else nr-1),(j-1 if j>0 else nc-1)]
se = q[(i+1 if i<nr-1 else 0),(j+1 if j<nc-1 else 0)]
ne = q[(i-1 if i>0 else nr-1),(j+1 if j<nc-1 else 0)]
sw = q[(i+1 if i<nr-1 else 0),(j-1 if j>0 else nc-1)]
q2 = [nw, se, ne, sw]
gbn[i,j] += SF * cell_boundary(n, q2, qmax)
gbs[i,j] += SF * cell_boundary(s, q2, qmax)
gbe[i,j] += SF * cell_boundary(e, q2, qmax)
gbw[i,j] += SF * cell_boundary(w, q2, qmax)
gbn[i,j] *= 1 + RP * np.random.random()
gbs[i,j] *= 1 + RP * np.random.random()
gbe[i,j] *= 1 + RP * np.random.random()
gbw[i,j] *= 1 + RP * np.random.random()
gb1 = [gbn[i,j], gbs[i,j], gbe[i,j], gbw[i,j]]
# find neighbour for which new boundary energy is minimum
m[i,j] = np.argmin(gb1)
# thermal energy
gt[i,j] = thermal(T)
# check if a cell will transform into some neighbour
t[i,j] = (q1.count(q[i,j]) != len(q1)) and (gt[i,j] + gb[i,j] >= GA)
if not t[i,j]:
continue
# pick orientation of neighbour with minimum new boundary energy
p[i,j] = q1[m[i,j]]
# check if the cell changed of orientation
if p[i,j] != q[i,j]:
changed = True
if plt:
plot_partial(gt, gb, [gbn, gbs, gbe, gbw], 'NSEW', m, t)
return p, changed
Too much repetitive code
Hard to understand what the model is doing
Easy to make mistakes
Slow
ARRAY PROGRAMMING
RP = 0.01 # random perturbation
SF = 0.25 # second-order-neighbours factor

## Slide 45: 2nd order neighbours (Python)
# new version of step_rnd which takes into account the influence of secon-order neighbours
def step_rnd2(q, qmax, T, plt):
nr, nc = q.shape # number of rows and columns
p, changed = np.copy(q), False # p is the map of product orientations
gt = np.zeros(q.shape) # thermal energy
gb = np.zeros(q.shape) # current grain boundary energy
gbn = np.zeros(q.shape) # new grain boundary energy if transforms into north neighbour
gbs = np.zeros(q.shape) # new grain boundary energy if transforms into south neighbour
gbe = np.zeros(q.shape) # new grain boundary energy if transforms into east neighbour
gbw = np.zeros(q.shape) # new grain boundary energy if transforms into west neighbour
m = np.zeros(q.shape, dtype=int) # neighbour for which new grain boundary energy is minimum
t = np.zeros(q.shape, dtype=bool) # cells that will transform
for i in range(nr):
for j in range(nc):
# 1st-order neighbours: north, south, east, west
n = q[(i-1 if i>0 else nr-1),j]
s = q[(i+1 if i<nr-1 else 0),j]
e = q[i,(j+1 if j<nc-1 else 0)]
w = q[i,(j-1 if j>0 else nc-1)]
q1 = [n, s, e, w]
# calculate current boundary energy
gb[i,j] = cell_boundary(q[i,j], q1, qmax)
# and when transforming into each neighbour
gbn[i,j] = cell_boundary(n, q1, qmax)
gbs[i,j] = cell_boundary(s, q1, qmax)
gbe[i,j] = cell_boundary(e, q1, qmax)
gbw[i,j] = cell_boundary(w, q1, qmax)
if SF > 0:
nw = q[(i-1 if i>0 else nr-1),(j-1 if j>0 else nc-1)]
se = q[(i+1 if i<nr-1 else 0),(j+1 if j<nc-1 else 0)]
ne = q[(i-1 if i>0 else nr-1),(j+1 if j<nc-1 else 0)]
sw = q[(i+1 if i<nr-1 else 0),(j-1 if j>0 else nc-1)]
q2 = [nw, se, ne, sw]
gbn[i,j] += SF * cell_boundary(n, q2, qmax)
gbs[i,j] += SF * cell_boundary(s, q2, qmax)
gbe[i,j] += SF * cell_boundary(e, q2, qmax)
gbw[i,j] += SF * cell_boundary(w, q2, qmax)
gbn[i,j] *= 1 + RP * np.random.random()
gbs[i,j] *= 1 + RP * np.random.random()
gbe[i,j] *= 1 + RP * np.random.random()
gbw[i,j] *= 1 + RP * np.random.random()
gb1 = [gbn[i,j], gbs[i,j], gbe[i,j], gbw[i,j]]
# find neighbour for which new boundary energy is minimum
m[i,j] = np.argmin(gb1)
# thermal energy
gt[i,j] = thermal(T)
# check if a cell will transform into some neighbour
t[i,j] = (q1.count(q[i,j]) != len(q1)) and (gt[i,j] + gb[i,j] >= GA)
if not t[i,j]:
continue
# pick orientation of neighbour with minimum new boundary energy
p[i,j] = q1[m[i,j]]
# check if the cell changed of orientation
if p[i,j] != q[i,j]:
changed = True
if plt:
plot_partial(gt, gb, [gbn, gbs, gbe, gbw], 'NSEW', m, t)
return p, changed
RP = 0.01 # random perturbation
SF = 0.25 # second-order-neighbours factor

## Slide 46: 2nd order neighbours (NumPy)
# new version of step_rnd2 using numpy functions
def step_numpy2(q, qmax, T, plt):
q1 = [np.roll(q, i, axis=a) for i, a in zip([-1,1,1,-1], [0,0,1,1])] # 1st-order neighbours
gt, gb = -R*T*np.log(1-np.random.random(q.shape)), boundary(q, q1, qmax) # thermal and boundary energies
gb1 = np.array([boundary(qi, q1, qmax) for qi in q1]) # new boundary energies
if SF > 0:
q2 = [np.roll(qi, i, axis=a) for qi, i, a in zip(q1, [-1,1,-1,1], [1,1,0,0])] # 2nd-order neighbours
gb1 += SF * np.array([boundary(qi, q2, qmax) for qi in q1]) # their boundary energies
gb1 *= 1 + RP * np.random.random(gb1.shape) # apply random perturbation
t, m = (gt + gb >= GA), np.argmin(gb1, axis=0) # cells to transform and minimum
p = np.where(t, np.choose(m, q1), q) # product orientations
if plt:
plot_partial(gt, gb, gb1, 'NSEW', m, t)
return p, not np.array_equal(q, p)
RP = 0.01 # random perturbation
SF = 0.25 # second-order-neighbours factor

## Slide 47: 2nd order neighbours (NumPy)
# new version of step_rnd2 using numpy functions
def step_numpy2(q, qmax, T, plt):
q1 = [np.roll(q, i, axis=a) for i, a in zip([-1,1,1,-1], [0,0,1,1])] # 1st-order neighbours
gt, gb = -R*T*np.log(1-np.random.random(q.shape)), boundary(q, q1, qmax) # thermal and boundary energies
gb1 = np.array([boundary(qi, q1, qmax) for qi in q1]) # new boundary energies
if SF > 0:
q2 = [np.roll(qi, i, axis=a) for qi, i, a in zip(q1, [-1,1,-1,1], [1,1,0,0])] # 2nd-order neighbours
gb1 += SF * np.array([boundary(qi, q2, qmax) for qi in q1]) # their boundary energies
gb1 *= 1 + RP * np.random.random(gb1.shape) # apply random perturbation
t, m = (gt + gb >= GA), np.argmin(gb1, axis=0) # cells to transform and minimum
p = np.where(t, np.choose(m, q1), q) # product orientations
if plt:
plot_partial(gt, gb, gb1, 'NSEW', m, t)
return p, not np.array_equal(q, p)
RP = 0.01 # random perturbation
SF = 0.25 # second-order-neighbours factor
Less code, less mistakes, more performance

## Slide 48: 2nd order neighbours (NumPy)
# new version of step_rnd2 using numpy functions
def step_numpy2(q, qmax, T, plt):
q1 = [np.roll(q, i, axis=a) for i, a in zip([-1,1,1,-1], [0,0,1,1])] # 1st-order neighbours
gt, gb = -R*T*np.log(1-np.random.random(q.shape)), boundary(q, q1, qmax) # thermal and boundary energies
gb1 = np.array([boundary(qi, q1, qmax) for qi in q1]) # new boundary energies
if SF > 0:
q2 = [np.roll(qi, i, axis=a) for qi, i, a in zip(q1, [-1,1,-1,1], [1,1,0,0])] # 2nd-order neighbours
gb1 += SF * np.array([boundary(qi, q2, qmax) for qi in q1]) # their boundary energies
gb1 *= 1 + RP * np.random.random(gb1.shape) # apply random perturbation
t, m = (gt + gb >= GA), np.argmin(gb1, axis=0) # cells to transform and minimum
p = np.where(t, np.choose(m, q1), q) # product orientations
if plt:
plot_partial(gt, gb, gb1, 'NSEW', m, t)
return p, not np.array_equal(q, p)
RP = 0.01 # random perturbation
SF = 0.25 # second-order-neighbours factor
Less code, less mistakes, more performance
Less likely to be written by students

## Slide 49: 2nd order neighbours (NumPy)
# new version of step_rnd2 using numpy functions
def step_numpy2(q, qmax, T, plt):
q1 = [np.roll(q, i, axis=a) for i, a in zip([-1,1,1,-1], [0,0,1,1])] # 1st-order neighbours
gt, gb = -R*T*np.log(1-np.random.random(q.shape)), boundary(q, q1, qmax) # thermal and boundary energies
gb1 = np.array([boundary(qi, q1, qmax) for qi in q1]) # new boundary energies
if SF > 0:
q2 = [np.roll(qi, i, axis=a) for qi, i, a in zip(q1, [-1,1,-1,1], [1,1,0,0])] # 2nd-order neighbours
gb1 += SF * np.array([boundary(qi, q2, qmax) for qi in q1]) # their boundary energies
gb1 *= 1 + RP * np.random.random(gb1.shape) # apply random perturbation
t, m = (gt + gb >= GA), np.argmin(gb1, axis=0) # cells to transform and minimum
p = np.where(t, np.choose(m, q1), q) # product orientations
if plt:
plot_partial(gt, gb, gb1, 'NSEW', m, t)
return p, not np.array_equal(q, p)
# return boundary energies for orientations q with neighbours q1
def boundary(q, q1, qmax):
dg = np.array([misorientation(q, qi, qmax) for qi in q1])
sin = np.sin(dg)
gbi = G0 * sin * (1 - np.log(sin, out=np.ones_like(dg), where=dg>0))
return np.sum(gbi, axis=0)
RP = 0.01 # random perturbation
SF = 0.25 # second-order-neighbours factor

## Slide 50: NumPy
Array objects
  The N-dimensional array (ndarray)
  Scalars
  Data type objects (dtype)
  Indexing routines
  Iterating over arrays
  Standard array subclasses
  Masked arrays
  The array interface protocol
  Datetimes and Timedeltas
Array API Standard Compatibility
  Table of Differences between numpy.array_api and numpy
Constants
  Inf
  Infinity
  NAN
  NINF
  NZERO
  NaN
  PINF
  PZERO
  e
  euler_gamma
  inf
  infty
  nan
  newaxis
  pi
Universal functions (ufunc)
  ufunc
  Available ufuncs
Routines
  Array creation routines
  Array manipulation routines
  Binary operations
  String operations
  C-Types foreign function interface (numpy.ctypeslib)
  Datetime support functions
  Data type routines
  Mathematical functions with automatic domain
  Floating point error handling
  Discrete Fourier Transform (numpy.fft)
  Functional programming
  NumPy-specific help functions
  Input and output
  Linear algebra (numpy.linalg)
  Logic functions
  Masked array operations
  Mathematical functions
  Matrix library (numpy.matlib)
  Miscellaneous routines
  Padding Arrays
  Polynomials
  Random sampling (numpy.random)
  Set routines
  Sorting, searching, and counting
  Statistics
  Test Support (numpy.testing)
  Support for testing overrides (numpy.testing.overrides)
  Window functions
Typing (numpy.typing)
  Mypy plugin
  Differences from the runtime NumPy API
  API
Global state
  Performance-related options
  Debugging-related options
  Testing planned future behavior
Packaging (numpy.distutils)
  Modules in numpy.distutils
  Configuration class
  Building Installable C libraries
  Conversion of .src files
NumPy distutils - users guide
  SciPy structure
  Requirements for SciPy packages
  The setup.py file
  The __init__.py file
  Extra features in NumPy Distutils
Status of numpy.distutils and migration advice
  Migration advice
  Interaction of numpy.distutils with setuptools
NumPy C-API
  Python Types and C-Structures
  System configuration
  Data Type API
  Array API
  Array Iterator API
  UFunc API
  Generalized Universal Function API
  NumPy core libraries
  C API Deprecations
  Memory management in NumPy
CPU/SIMD Optimizations
  CPU build options
  How does the CPU dispatcher work?
NumPy security
  Advice for using NumPy on untrusted data
NumPy and SWIG
  numpy.i: a SWIG Interface File for NumPy
  Testing the numpy.i Typemaps

## Slide 51: NumPy
Array objects
  The N-dimensional array (ndarray)
  Scalars
  Data type objects (dtype)
  Indexing routines
  Iterating over arrays
  Standard array subclasses
  Masked arrays
  The array interface protocol
  Datetimes and Timedeltas
Array API Standard Compatibility
  Table of Differences between numpy.array_api and numpy
Constants
  Inf
  Infinity
  NAN
  NINF
  NZERO
  NaN
  PINF
  PZERO
  e
  euler_gamma
  inf
  infty
  nan
  newaxis
  pi
Universal functions (ufunc)
  ufunc
  Available ufuncs
Routines
  Array creation routines
  Array manipulation routines
  Binary operations
  String operations
  C-Types foreign function interface (numpy.ctypeslib)
  Datetime support functions
  Data type routines
  Mathematical functions with automatic domain
  Floating point error handling
  Discrete Fourier Transform (numpy.fft)
  Functional programming
  NumPy-specific help functions
  Input and output
  Linear algebra (numpy.linalg)
  Logic functions
  Masked array operations
  Mathematical functions
  Matrix library (numpy.matlib)
  Miscellaneous routines
  Padding Arrays
  Polynomials
  Random sampling (numpy.random)
  Set routines
  Sorting, searching, and counting
  Statistics
  Test Support (numpy.testing)
  Support for testing overrides (numpy.testing.overrides)
  Window functions
Typing (numpy.typing)
  Mypy plugin
  Differences from the runtime NumPy API
  API
Global state
  Performance-related options
  Debugging-related options
  Testing planned future behavior
Packaging (numpy.distutils)
  Modules in numpy.distutils
  Configuration class
  Building Installable C libraries
  Conversion of .src files
NumPy distutils - users guide
  SciPy structure
  Requirements for SciPy packages
  The setup.py file
  The __init__.py file
  Extra features in NumPy Distutils
Status of numpy.distutils and migration advice
  Migration advice
  Interaction of numpy.distutils with setuptools
NumPy C-API
  Python Types and C-Structures
  System configuration
  Data Type API
  Array API
  Array Iterator API
  UFunc API
  Generalized Universal Function API
  NumPy core libraries
  C API Deprecations
  Memory management in NumPy
CPU/SIMD Optimizations
  CPU build options
  How does the CPU dispatcher work?
NumPy security
  Advice for using NumPy on untrusted data
NumPy and SWIG
  numpy.i: a SWIG Interface File for NumPy
  Testing the numpy.i Typemaps
Available ufuncs
Math operations
add(x1, x2, /[, out, where, casting, order, ...])
subtract(x1, x2, /[, out, where, casting, ...])
multiply(x1, x2, /[, out, where, casting, ...])
matmul(x1, x2, /[, out, casting, order, ...])
divide(x1, x2, /[, out, where, casting, ...])
logaddexp(x1, x2, /[, out, where, casting, ...])
logaddexp2(x1, x2, /[, out, where, casting, ...])
true_divide(x1, x2, /[, out, where, ...])
floor_divide(x1, x2, /[, out, where, ...])
negative(x, /[, out, where, casting, order, ...])
positive(x, /[, out, where, casting, order, ...])
power(x1, x2, /[, out, where, casting, ...])
float_power(x1, x2, /[, out, where, ...])
remainder(x1, x2, /[, out, where, casting, ...])
mod(x1, x2, /[, out, where, casting, order, ...])
fmod(x1, x2, /[, out, where, casting, ...])
divmod(x1, x2[, out1, out2], / [[, out, ...])
absolute(x, /[, out, where, casting, order, ...])
fabs(x, /[, out, where, casting, order, ...])
rint(x, /[, out, where, casting, order, ...])
sign(x, /[, out, where, casting, order, ...])
heaviside(x1, x2, /[, out, where, casting, ...])
conj(x, /[, out, where, casting, order, ...])
conjugate(x, /[, out, where, casting, ...])
exp(x, /[, out, where, casting, order, ...])
exp2(x, /[, out, where, casting, order, ...])
log(x, /[, out, where, casting, order, ...])
log2(x, /[, out, where, casting, order, ...])
log10(x, /[, out, where, casting, order, ...])
expm1(x, /[, out, where, casting, order, ...])
log1p(x, /[, out, where, casting, order, ...])
sqrt(x, /[, out, where, casting, order, ...])
square(x, /[, out, where, casting, order, ...])
cbrt(x, /[, out, where, casting, order, ...])
reciprocal(x, /[, out, where, casting, ...])
gcd(x1, x2, /[, out, where, casting, order, ...])
lcm(x1, x2, /[, out, where, casting, order, ...])
Trigonometric functions
sin(x, /[, out, where, casting, order, ...])
cos(x, /[, out, where, casting, order, ...])
tan(x, /[, out, where, casting, order, ...])
arcsin(x, /[, out, where, casting, order, ...])
arccos(x, /[, out, where, casting, order, ...])
arctan(x, /[, out, where, casting, order, ...])
arctan2(x1, x2, /[, out, where, casting, ...])
hypot(x1, x2, /[, out, where, casting, ...])
sinh(x, /[, out, where, casting, order, ...])
cosh(x, /[, out, where, casting, order, ...])
tanh(x, /[, out, where, casting, order, ...])
arcsinh(x, /[, out, where, casting, order, ...])
arccosh(x, /[, out, where, casting, order, ...])
arctanh(x, /[, out, where, casting, order, ...])
degrees(x, /[, out, where, casting, order, ...])
radians(x, /[, out, where, casting, order, ...])
deg2rad(x, /[, out, where, casting, order, ...])
rad2deg(x, /[, out, where, casting, order, ...])
Bit-twiddling functions
bitwise_and(x1, x2, /[, out, where, ...])
bitwise_or(x1, x2, /[, out, where, casting, ...])
bitwise_xor(x1, x2, /[, out, where, ...])
invert(x, /[, out, where, casting, order, ...])
left_shift(x1, x2, /[, out, where, casting, ...])
right_shift(x1, x2, /[, out, where, ...])
Comparison functions
greater(x1, x2, /[, out, where, casting, ...])
greater_equal(x1, x2, /[, out, where, ...])
less(x1, x2, /[, out, where, casting, ...])
less_equal(x1, x2, /[, out, where, casting, ...])
not_equal(x1, x2, /[, out, where, casting, ...])
equal(x1, x2, /[, out, where, casting, ...])
logical_and(x1, x2, /[, out, where, ...])
logical_or(x1, x2, /[, out, where, casting, ...])
logical_xor(x1, x2, /[, out, where, ...])
logical_not(x, /[, out, where, casting, ...])
maximum(x1, x2, /[, out, where, casting, ...])
minimum(x1, x2, /[, out, where, casting, ...])
fmax(x1, x2, /[, out, where, casting, ...])
fmin(x1, x2, /[, out, where, casting, ...])
Floating functions
isfinite(x, /[, out, where, casting, order, ...])
isinf(x, /[, out, where, casting, order, ...])
isnan(x, /[, out, where, casting, order, ...])
isnat(x, /[, out, where, casting, order, ...])
fabs(x, /[, out, where, casting, order, ...])
signbit(x, /[, out, where, casting, order, ...])
copysign(x1, x2, /[, out, where, casting, ...])
nextafter(x1, x2, /[, out, where, casting, ...])
spacing(x, /[, out, where, casting, order, ...])
modf(x[, out1, out2], / [[, out, where, ...])
ldexp(x1, x2, /[, out, where, casting, ...])
frexp(x[, out1, out2], / [[, out, where, ...])
fmod(x1, x2, /[, out, where, casting, ...])
floor(x, /[, out, where, casting, order, ...])
ceil(x, /[, out, where, casting, order, ...])
trunc(x, /[, out, where, casting, order, ...])

## Slide 52: NumPy
Array objects
  The N-dimensional array (ndarray)
  Scalars
  Data type objects (dtype)
  Indexing routines
  Iterating over arrays
  Standard array subclasses
  Masked arrays
  The array interface protocol
  Datetimes and Timedeltas
Array API Standard Compatibility
  Table of Differences between numpy.array_api and numpy
Constants
  Inf
  Infinity
  NAN
  NINF
  NZERO
  NaN
  PINF
  PZERO
  e
  euler_gamma
  inf
  infty
  nan
  newaxis
  pi
Universal functions (ufunc)
  ufunc
  Available ufuncs
Routines
  Array creation routines
  Array manipulation routines
  Binary operations
  String operations
  C-Types foreign function interface (numpy.ctypeslib)
  Datetime support functions
  Data type routines
  Mathematical functions with automatic domain
  Floating point error handling
  Discrete Fourier Transform (numpy.fft)
  Functional programming
  NumPy-specific help functions
  Input and output
  Linear algebra (numpy.linalg)
  Logic functions
  Masked array operations
  Mathematical functions
  Matrix library (numpy.matlib)
  Miscellaneous routines
  Padding Arrays
  Polynomials
  Random sampling (numpy.random)
  Set routines
  Sorting, searching, and counting
  Statistics
  Test Support (numpy.testing)
  Support for testing overrides (numpy.testing.overrides)
  Window functions
Typing (numpy.typing)
  Mypy plugin
  Differences from the runtime NumPy API
  API
Global state
  Performance-related options
  Debugging-related options
  Testing planned future behavior
Packaging (numpy.distutils)
  Modules in numpy.distutils
  Configuration class
  Building Installable C libraries
  Conversion of .src files
NumPy distutils - users guide
  SciPy structure
  Requirements for SciPy packages
  The setup.py file
  The __init__.py file
  Extra features in NumPy Distutils
Status of numpy.distutils and migration advice
  Migration advice
  Interaction of numpy.distutils with setuptools
NumPy C-API
  Python Types and C-Structures
  System configuration
  Data Type API
  Array API
  Array Iterator API
  UFunc API
  Generalized Universal Function API
  NumPy core libraries
  C API Deprecations
  Memory management in NumPy
CPU/SIMD Optimizations
  CPU build options
  How does the CPU dispatcher work?
NumPy security
  Advice for using NumPy on untrusted data
NumPy and SWIG
  numpy.i: a SWIG Interface File for NumPy
  Testing the numpy.i Typemaps
Available ufuncs
Math operations
add(x1, x2, /[, out, where, casting, order, ...])
subtract(x1, x2, /[, out, where, casting, ...])
multiply(x1, x2, /[, out, where, casting, ...])
matmul(x1, x2, /[, out, casting, order, ...])
divide(x1, x2, /[, out, where, casting, ...])
logaddexp(x1, x2, /[, out, where, casting, ...])
logaddexp2(x1, x2, /[, out, where, casting, ...])
true_divide(x1, x2, /[, out, where, ...])
floor_divide(x1, x2, /[, out, where, ...])
negative(x, /[, out, where, casting, order, ...])
positive(x, /[, out, where, casting, order, ...])
power(x1, x2, /[, out, where, casting, ...])
float_power(x1, x2, /[, out, where, ...])
remainder(x1, x2, /[, out, where, casting, ...])
mod(x1, x2, /[, out, where, casting, order, ...])
fmod(x1, x2, /[, out, where, casting, ...])
divmod(x1, x2[, out1, out2], / [[, out, ...])
absolute(x, /[, out, where, casting, order, ...])
fabs(x, /[, out, where, casting, order, ...])
rint(x, /[, out, where, casting, order, ...])
sign(x, /[, out, where, casting, order, ...])
heaviside(x1, x2, /[, out, where, casting, ...])
conj(x, /[, out, where, casting, order, ...])
conjugate(x, /[, out, where, casting, ...])
exp(x, /[, out, where, casting, order, ...])
exp2(x, /[, out, where, casting, order, ...])
log(x, /[, out, where, casting, order, ...])
log2(x, /[, out, where, casting, order, ...])
log10(x, /[, out, where, casting, order, ...])
expm1(x, /[, out, where, casting, order, ...])
log1p(x, /[, out, where, casting, order, ...])
sqrt(x, /[, out, where, casting, order, ...])
square(x, /[, out, where, casting, order, ...])
cbrt(x, /[, out, where, casting, order, ...])
reciprocal(x, /[, out, where, casting, ...])
gcd(x1, x2, /[, out, where, casting, order, ...])
lcm(x1, x2, /[, out, where, casting, order, ...])
Trigonometric functions
sin(x, /[, out, where, casting, order, ...])
cos(x, /[, out, where, casting, order, ...])
tan(x, /[, out, where, casting, order, ...])
arcsin(x, /[, out, where, casting, order, ...])
arccos(x, /[, out, where, casting, order, ...])
arctan(x, /[, out, where, casting, order, ...])
arctan2(x1, x2, /[, out, where, casting, ...])
hypot(x1, x2, /[, out, where, casting, ...])
sinh(x, /[, out, where, casting, order, ...])
cosh(x, /[, out, where, casting, order, ...])
tanh(x, /[, out, where, casting, order, ...])
arcsinh(x, /[, out, where, casting, order, ...])
arccosh(x, /[, out, where, casting, order, ...])
arctanh(x, /[, out, where, casting, order, ...])
degrees(x, /[, out, where, casting, order, ...])
radians(x, /[, out, where, casting, order, ...])
deg2rad(x, /[, out, where, casting, order, ...])
rad2deg(x, /[, out, where, casting, order, ...])
Bit-twiddling functions
bitwise_and(x1, x2, /[, out, where, ...])
bitwise_or(x1, x2, /[, out, where, casting, ...])
bitwise_xor(x1, x2, /[, out, where, ...])
invert(x, /[, out, where, casting, order, ...])
left_shift(x1, x2, /[, out, where, casting, ...])
right_shift(x1, x2, /[, out, where, ...])
Comparison functions
greater(x1, x2, /[, out, where, casting, ...])
greater_equal(x1, x2, /[, out, where, ...])
less(x1, x2, /[, out, where, casting, ...])
less_equal(x1, x2, /[, out, where, casting, ...])
not_equal(x1, x2, /[, out, where, casting, ...])
equal(x1, x2, /[, out, where, casting, ...])
logical_and(x1, x2, /[, out, where, ...])
logical_or(x1, x2, /[, out, where, casting, ...])
logical_xor(x1, x2, /[, out, where, ...])
logical_not(x, /[, out, where, casting, ...])
maximum(x1, x2, /[, out, where, casting, ...])
minimum(x1, x2, /[, out, where, casting, ...])
fmax(x1, x2, /[, out, where, casting, ...])
fmin(x1, x2, /[, out, where, casting, ...])
Floating functions
isfinite(x, /[, out, where, casting, order, ...])
isinf(x, /[, out, where, casting, order, ...])
isnan(x, /[, out, where, casting, order, ...])
isnat(x, /[, out, where, casting, order, ...])
fabs(x, /[, out, where, casting, order, ...])
signbit(x, /[, out, where, casting, order, ...])
copysign(x1, x2, /[, out, where, casting, ...])
nextafter(x1, x2, /[, out, where, casting, ...])
spacing(x, /[, out, where, casting, order, ...])
modf(x[, out1, out2], / [[, out, where, ...])
ldexp(x1, x2, /[, out, where, casting, ...])
frexp(x[, out1, out2], / [[, out, where, ...])
fmod(x1, x2, /[, out, where, casting, ...])
floor(x, /[, out, where, casting, order, ...])
ceil(x, /[, out, where, casting, order, ...])
trunc(x, /[, out, where, casting, order, ...])
Array objects
The N-dimensional array (ndarray)
  Constructing arrays
  Indexing arrays
  Internal memory layout of an ndarray
  Array attributes
  Array methods
  Arithmetic, matrix multiplication, and comparison operations
  Special methods
Scalars
  Built-in scalar types
  Attributes
  Indexing
  Methods
  Defining new types
Data type objects (dtype)
  Specifying and constructing data types
  dtype
Indexing routines
  Generating index arrays
  Indexing-like operations
  Inserting data into arrays
  Iterating over arrays
Iterating over arrays
  Single array iteration
  Broadcasting array iteration
  Putting the Inner Loop in Cython
Standard array subclasses
  Special attributes and methods
  Matrix objects
  Memory-mapped file arrays
  Character arrays (numpy.char)
  Record arrays (numpy.rec)
  Masked arrays (numpy.ma)
  Standard container class
  Array Iterators
Masked arrays
  The numpy.ma module
  Using numpy.ma
  Examples
  Constants of the numpy.ma module
  The MaskedArray class
  MaskedArray methods
  Masked array operations
The array interface protocol
  Python side
  C-struct access
  Type description examples
  Differences with Array interface (Version 2)
Datetimes and Timedeltas
  Datetime64 Conventions and Assumptions
  Basic Datetimes
  Datetime and Timedelta Arithmetic
  Datetime Units
  Business Day Functionality
  Datetime64 shortcomings

## Slide 53: NumPy
Array objects
  The N-dimensional array (ndarray)
  Scalars
  Data type objects (dtype)
  Indexing routines
  Iterating over arrays
  Standard array subclasses
  Masked arrays
  The array interface protocol
  Datetimes and Timedeltas
Array API Standard Compatibility
  Table of Differences between numpy.array_api and numpy
Constants
  Inf
  Infinity
  NAN
  NINF
  NZERO
  NaN
  PINF
  PZERO
  e
  euler_gamma
  inf
  infty
  nan
  newaxis
  pi
Universal functions (ufunc)
  ufunc
  Available ufuncs
Routines
  Array creation routines
  Array manipulation routines
  Binary operations
  String operations
  C-Types foreign function interface (numpy.ctypeslib)
  Datetime support functions
  Data type routines
  Mathematical functions with automatic domain
  Floating point error handling
  Discrete Fourier Transform (numpy.fft)
  Functional programming
  NumPy-specific help functions
  Input and output
  Linear algebra (numpy.linalg)
  Logic functions
  Masked array operations
  Mathematical functions
  Matrix library (numpy.matlib)
  Miscellaneous routines
  Padding Arrays
  Polynomials
  Random sampling (numpy.random)
  Set routines
  Sorting, searching, and counting
  Statistics
  Test Support (numpy.testing)
  Support for testing overrides (numpy.testing.overrides)
  Window functions
Typing (numpy.typing)
  Mypy plugin
  Differences from the runtime NumPy API
  API
Global state
  Performance-related options
  Debugging-related options
  Testing planned future behavior
Packaging (numpy.distutils)
  Modules in numpy.distutils
  Configuration class
  Building Installable C libraries
  Conversion of .src files
NumPy distutils - users guide
  SciPy structure
  Requirements for SciPy packages
  The setup.py file
  The __init__.py file
  Extra features in NumPy Distutils
Status of numpy.distutils and migration advice
  Migration advice
  Interaction of numpy.distutils with setuptools
NumPy C-API
  Python Types and C-Structures
  System configuration
  Data Type API
  Array API
  Array Iterator API
  UFunc API
  Generalized Universal Function API
  NumPy core libraries
  C API Deprecations
  Memory management in NumPy
CPU/SIMD Optimizations
  CPU build options
  How does the CPU dispatcher work?
NumPy security
  Advice for using NumPy on untrusted data
NumPy and SWIG
  numpy.i: a SWIG Interface File for NumPy
  Testing the numpy.i Typemaps
Available ufuncs
Math operations
add(x1, x2, /[, out, where, casting, order, ...])
subtract(x1, x2, /[, out, where, casting, ...])
multiply(x1, x2, /[, out, where, casting, ...])
matmul(x1, x2, /[, out, casting, order, ...])
divide(x1, x2, /[, out, where, casting, ...])
logaddexp(x1, x2, /[, out, where, casting, ...])
logaddexp2(x1, x2, /[, out, where, casting, ...])
true_divide(x1, x2, /[, out, where, ...])
floor_divide(x1, x2, /[, out, where, ...])
negative(x, /[, out, where, casting, order, ...])
positive(x, /[, out, where, casting, order, ...])
power(x1, x2, /[, out, where, casting, ...])
float_power(x1, x2, /[, out, where, ...])
remainder(x1, x2, /[, out, where, casting, ...])
mod(x1, x2, /[, out, where, casting, order, ...])
fmod(x1, x2, /[, out, where, casting, ...])
divmod(x1, x2[, out1, out2], / [[, out, ...])
absolute(x, /[, out, where, casting, order, ...])
fabs(x, /[, out, where, casting, order, ...])
rint(x, /[, out, where, casting, order, ...])
sign(x, /[, out, where, casting, order, ...])
heaviside(x1, x2, /[, out, where, casting, ...])
conj(x, /[, out, where, casting, order, ...])
conjugate(x, /[, out, where, casting, ...])
exp(x, /[, out, where, casting, order, ...])
exp2(x, /[, out, where, casting, order, ...])
log(x, /[, out, where, casting, order, ...])
log2(x, /[, out, where, casting, order, ...])
log10(x, /[, out, where, casting, order, ...])
expm1(x, /[, out, where, casting, order, ...])
log1p(x, /[, out, where, casting, order, ...])
sqrt(x, /[, out, where, casting, order, ...])
square(x, /[, out, where, casting, order, ...])
cbrt(x, /[, out, where, casting, order, ...])
reciprocal(x, /[, out, where, casting, ...])
gcd(x1, x2, /[, out, where, casting, order, ...])
lcm(x1, x2, /[, out, where, casting, order, ...])
Trigonometric functions
sin(x, /[, out, where, casting, order, ...])
cos(x, /[, out, where, casting, order, ...])
tan(x, /[, out, where, casting, order, ...])
arcsin(x, /[, out, where, casting, order, ...])
arccos(x, /[, out, where, casting, order, ...])
arctan(x, /[, out, where, casting, order, ...])
arctan2(x1, x2, /[, out, where, casting, ...])
hypot(x1, x2, /[, out, where, casting, ...])
sinh(x, /[, out, where, casting, order, ...])
cosh(x, /[, out, where, casting, order, ...])
tanh(x, /[, out, where, casting, order, ...])
arcsinh(x, /[, out, where, casting, order, ...])
arccosh(x, /[, out, where, casting, order, ...])
arctanh(x, /[, out, where, casting, order, ...])
degrees(x, /[, out, where, casting, order, ...])
radians(x, /[, out, where, casting, order, ...])
deg2rad(x, /[, out, where, casting, order, ...])
rad2deg(x, /[, out, where, casting, order, ...])
Bit-twiddling functions
bitwise_and(x1, x2, /[, out, where, ...])
bitwise_or(x1, x2, /[, out, where, casting, ...])
bitwise_xor(x1, x2, /[, out, where, ...])
invert(x, /[, out, where, casting, order, ...])
left_shift(x1, x2, /[, out, where, casting, ...])
right_shift(x1, x2, /[, out, where, ...])
Comparison functions
greater(x1, x2, /[, out, where, casting, ...])
greater_equal(x1, x2, /[, out, where, ...])
less(x1, x2, /[, out, where, casting, ...])
less_equal(x1, x2, /[, out, where, casting, ...])
not_equal(x1, x2, /[, out, where, casting, ...])
equal(x1, x2, /[, out, where, casting, ...])
logical_and(x1, x2, /[, out, where, ...])
logical_or(x1, x2, /[, out, where, casting, ...])
logical_xor(x1, x2, /[, out, where, ...])
logical_not(x, /[, out, where, casting, ...])
maximum(x1, x2, /[, out, where, casting, ...])
minimum(x1, x2, /[, out, where, casting, ...])
fmax(x1, x2, /[, out, where, casting, ...])
fmin(x1, x2, /[, out, where, casting, ...])
Floating functions
isfinite(x, /[, out, where, casting, order, ...])
isinf(x, /[, out, where, casting, order, ...])
isnan(x, /[, out, where, casting, order, ...])
isnat(x, /[, out, where, casting, order, ...])
fabs(x, /[, out, where, casting, order, ...])
signbit(x, /[, out, where, casting, order, ...])
copysign(x1, x2, /[, out, where, casting, ...])
nextafter(x1, x2, /[, out, where, casting, ...])
spacing(x, /[, out, where, casting, order, ...])
modf(x[, out1, out2], / [[, out, where, ...])
ldexp(x1, x2, /[, out, where, casting, ...])
frexp(x[, out1, out2], / [[, out, where, ...])
fmod(x1, x2, /[, out, where, casting, ...])
floor(x, /[, out, where, casting, order, ...])
ceil(x, /[, out, where, casting, order, ...])
trunc(x, /[, out, where, casting, order, ...])
Array objects
The N-dimensional array (ndarray)
  Constructing arrays
  Indexing arrays
  Internal memory layout of an ndarray
  Array attributes
  Array methods
  Arithmetic, matrix multiplication, and comparison operations
  Special methods
Scalars
  Built-in scalar types
  Attributes
  Indexing
  Methods
  Defining new types
Data type objects (dtype)
  Specifying and constructing data types
  dtype
Indexing routines
  Generating index arrays
  Indexing-like operations
  Inserting data into arrays
  Iterating over arrays
Iterating over arrays
  Single array iteration
  Broadcasting array iteration
  Putting the Inner Loop in Cython
Standard array subclasses
  Special attributes and methods
  Matrix objects
  Memory-mapped file arrays
  Character arrays (numpy.char)
  Record arrays (numpy.rec)
  Masked arrays (numpy.ma)
  Standard container class
  Array Iterators
Masked arrays
  The numpy.ma module
  Using numpy.ma
  Examples
  Constants of the numpy.ma module
  The MaskedArray class
  MaskedArray methods
  Masked array operations
The array interface protocol
  Python side
  C-struct access
  Type description examples
  Differences with Array interface (Version 2)
Datetimes and Timedeltas
  Datetime64 Conventions and Assumptions
  Basic Datetimes
  Datetime and Timedelta Arithmetic
  Datetime Units
  Business Day Functionality
  Datetime64 shortcomings
Routines
Array creation routines
  From shape or value
  From existing data
  Creating record arrays (numpy.rec)
  Creating character arrays (numpy.char)
  Numerical ranges
  Building matrices
  The Matrix class
Array manipulation routines
  Basic operations
  Changing array shape
  Transpose-like operations
  Changing number of dimensions
  Changing kind of array
  Joining arrays
  Splitting arrays
  Tiling arrays
  Adding and removing elements
  Rearranging elements
Binary operations
  Elementwise bit operations
  Bit packing
  Output formatting
String operations
  String operations
  Comparison
  String information
  Convenience class
C-Types foreign function interface (numpy.ctypeslib)
  as_array
  as_ctypes
  as_ctypes_type
  load_library
  ndpointer
  c_intp
Datetime support functions
  numpy.datetime_as_string
  numpy.datetime_data
  Business day functions
Data type routines
  numpy.can_cast
  numpy.promote_types
  numpy.min_scalar_type
  numpy.result_type
  numpy.common_type
  numpy.obj2sctype
  Creating data types
  Data type information
  Data type testing
  Miscellaneous
Mathematical functions with automatic domain
  Functions
Floating point error handling
  Setting and getting error handling
  Internal functions
Discrete Fourier Transform (numpy.fft)
  Standard FFTs
  Real FFTs
  Hermitian FFTs
  Helper routines
  Background information
  Implementation details
  Type Promotion
  Normalization
  Real and Hermitian transforms
  Higher dimensions
  References
  Examples
Functional programming
  numpy.apply_along_axis
  numpy.apply_over_axes
  numpy.vectorize
  numpy.frompyfunc
  numpy.piecewise
NumPy-specific help functions
  Finding help
  Reading help
Input and output
  NumPy binary files (NPY, NPZ)
  Text files
  Raw binary files
  String formatting
  Memory mapping files
  Text formatting options
  Base-n representations
  Data sources
  Binary format description
Linear algebra (numpy.linalg)
  The @ operator
  Matrix and vector products
  Decompositions
  Matrix eigenvalues
  Norms and other numbers
  Solving equations and inverting matrices
  Exceptions
  Linear algebra on several matrices at once
Logic functions
  Truth value testing
  Array contents
  Array type testing
  Logical operations
  Comparison
Masked array operations
  Constants
  Creation
  Inspecting the array
  Manipulating a MaskedArray
  Operations on masks
  Conversion operations
  Masked arrays arithmetic
Mathematical functions
  Trigonometric functions
  Hyperbolic functions
  Rounding
  Sums, products, differences
  Exponents and logarithms
  Other special functions
  Floating point routines
  Rational routines
  Arithmetic operations
  Handling complex numbers
  Extrema Finding
  Miscellaneous
Matrix library (numpy.matlib)
  numpy.matlib.empty
  numpy.matlib.zeros
  numpy.matlib.ones
  numpy.matlib.eye
  numpy.matlib.identity
  numpy.matlib.repmat
  numpy.matlib.rand
  numpy.matlib.randn
Miscellaneous routines
  Performance tuning
  Memory ranges
  Array mixins
  NumPy version comparison
  Utility
  Matlab-like Functions
Padding Arrays
  numpy.pad
Polynomials
  Transitioning from numpy.poly1d to numpy.polynomial
  Documentation for the polynomial Package
  Documentation for Legacy Polynomials
Random sampling (numpy.random)
  Quick Start
  Design
  Concepts
  Features
Set routines
  numpy.lib.arraysetops
  Making proper sets
  Boolean operations
Sorting, searching, and counting
  Sorting
  Searching
  Counting
Statistics
  Order statistics
  Averages and variances
  Correlating
  Histograms
Test Support (numpy.testing)
  Asserts
  Asserts (not recommended)
  Decorators
  Test Running
  Guidelines
Support for testing overrides (numpy.testing.overrides)
  Utility Functions
Window functions
  Various windows

## Slide 54: Learning Python might be easy

## Slide 55: Learning Python might be easy
Mastering NumPy is hard

## Slide 57
Mathematics + - × ÷ ⌈ ⌊ * ! | ⍟ ○ ⌹ ⊥ ⊤ ?
Logic and Comparison ~ ∧ ∨ ⍲ ⍱ < > ≤ ≥ = ≠ ≡ ≢
Structural ⍴ , ⍪ ⌽ ⊖ ⍉ ↑ ↓ ⊂ ⊆ ≡ ≢ ∊
Selection and Sets [] ⌷ ⊃ / ⌿ \ ⍀ ~ ≠ ∪ ∩ ⊣ ⊢
Search and Ordering ⍳ ⍸ ∊ ⍷ ⍋ ⍒
Operators ¨ ⍨ ⍣ . ∘ / \ ⌿ ⍀ ⌸ ⍤ ⍥ ⌺ @ ⍠ []
Dfns and dops ∇ ⍺ ⍵ ∇∇ ⍺⍺ ⍵⍵ {}
Miscellaneous ¯ ← → ⍬ ⍎ ⍕ ⋄ ⍝ ⎕ ⍞ ⌶ & # ()

## Slide 58: APL Grain Growth Model

## Slide 59: APL Grain Growth Model
gg←{
area←{0=⊃⍵:+/0≠,⍵ ⋄ (⍳2)×.((≢,⍵){⍺⍺÷1⌈+/,⍵≠1⌽[⍺]⍵})⊂⍵}
boundary←(⌈/,⍵){+⌿G0×s×1-⍟@(0∘<)s←1○○|↑(⍵-⊂⍺)÷2×⍺⍺}
step←{gt←-R×⍺×⍟?≠⍨⍵ ⋄ gb←⍵ boundary⊢q1←1 ¯1(⊖¨,⌽¨)⊂⍵ ⋄ t←(⊃(⊂⍵)∨.≠q1)∧GA≤gt+gb
gb1←(1+RP×?≠⍨q1)×{⍵+SF×q1 boundary¨⊂1 ¯1(⊖¨∘(2↓⊢),⌽¨∘(2↓⌽))q1}⍣(SF>0)boundary¨∘⊂⍨q1
m←⊃∘⍋⍤1⍉↑gb1 ⋄ (t/⍥,⍉m⌷⍤0 1⍉↑q1)@(t⍨)⍵}
R←8.314 ⋄ (GA G0 SF RP)←⍺⍺ ⋄ ⊃{⍺(2×(⍵÷○1)*÷2)}/⍺{q((⊃⌽⍵),area⊢q←⍺ step⊃⍵)}⍣⍵⍵⊢⍵(area ⍵)
}

## Slide 60: APL Grain Growth Model
gg←{
area←{0=⊃⍵:+/0≠,⍵ ⋄ (⍳2)×.((≢,⍵){⍺⍺÷1⌈+/,⍵≠1⌽[⍺]⍵})⊂⍵}
boundary←(⌈/,⍵){+⌿G0×s×1-⍟@(0∘<)s←1○○|↑(⍵-⊂⍺)÷2×⍺⍺}
step←{gt←-R×⍺×⍟?≠⍨⍵ ⋄ gb←⍵ boundary⊢q1←1 ¯1(⊖¨,⌽¨)⊂⍵ ⋄ t←(⊃(⊂⍵)∨.≠q1)∧GA≤gt+gb
gb1←(1+RP×?≠⍨q1)×{⍵+SF×q1 boundary¨⊂1 ¯1(⊖¨∘(2↓⊢),⌽¨∘(2↓⌽))q1}⍣(SF>0)boundary¨∘⊂⍨q1
m←⊃∘⍋⍤1⍉↑gb1 ⋄ (t/⍥,⍉m⌷⍤0 1⍉↑q1)@(t⍨)⍵}
R←8.314 ⋄ (GA G0 SF RP)←⍺⍺ ⋄ ⊃{⍺(2×(⍵÷○1)*÷2)}/⍺{q((⊃⌽⍵),area⊢q←⍺ step⊃⍵)}⍣⍵⍵⊢⍵(area ⍵)
}
Whole solution: step calculation, solve, calculate average diameter
Only APL primitives, no external libraries or system commands
Partial results available in the interpreter

## Slide 61: APL Grain Growth Model
gg←{
area←{0=⊃⍵:+/0≠,⍵ ⋄ (⍳2)×.((≢,⍵){⍺⍺÷1⌈+/,⍵≠1⌽[⍺]⍵})⊂⍵}
boundary←(⌈/,⍵){+⌿G0×s×1-⍟@(0∘<)s←1○○|↑(⍵-⊂⍺)÷2×⍺⍺}
step←{gt←-R×⍺×⍟?≠⍨⍵ ⋄ gb←⍵ boundary⊢q1←1 ¯1(⊖¨,⌽¨)⊂⍵ ⋄ t←(⊃(⊂⍵)∨.≠q1)∧GA≤gt+gb
gb1←(1+RP×?≠⍨q1)×{⍵+SF×q1 boundary¨⊂1 ¯1(⊖¨∘(2↓⊢),⌽¨∘(2↓⌽))q1}⍣(SF>0)boundary¨∘⊂⍨q1
m←⊃∘⍋⍤1⍉↑gb1 ⋄ (t/⍥,⍉m⌷⍤0 1⍉↑q1)@(t⍨)⍵}
R←8.314 ⋄ (GA G0 SF RP)←⍺⍺ ⋄ ⊃{⍺(2×(⍵÷○1)*÷2)}/⍺{q((⊃⌽⍵),area⊢q←⍺ step⊃⍵)}⍣⍵⍵⊢⍵(area ⍵)
}
Whole solution: step calculation, solve, calculate average diameter
Only APL primitives (no external libraries or system commands)
Partial results available in the interpreter
gg←{ ⍝ ⍺⍺: parameters (GA, G0, SF, RP), ⍵⍵: repetitions, ⍺: temperature, ⍵: initial orientations
R←8.314 ⍝ ideal gas constant
(GA G0 SF RP)←⍺⍺ ⍝ simulation parameters
qmax←⌈/,⍵ ⍝ maximum orientation
misorientations←{○|↑(⍵-⊂⍺)÷2×qmax} ⍝ ⍺: orientations, ⍵: neighbour orientations
⍝ return misorientations in radians
boundary←{ ⍝ ⍺: orientations, ⍵: list of neighbours orientations
s←1○⍺ misorientations ⍵ ⍝ sin of misorientation angle
+⌿G0×s×1-⍟@{0<⍵}s ⍝ return sum of all boundary energies (Read-Shockley)
}
boundary2←{ ⍝ ⍵: list of 1st-order neighbours orientations
SF≤0:0 ⍝ return zero if SF is not positive
q2←(1 ¯1⊖¨2↑⍵),1 ¯1⌽¨2↑⌽⍵ ⍝ orientations of 2nd-order neighbours
SF×⍵ boundary¨⊂q2 ⍝ return boundary energy of 2nd-order neighbours
}
step←{ ⍝ ⍺: temperature, ⍵: orientations
gt←-R×⍺×⍟?≠⍨⍵ ⍝ thermal energy
q1←(1 ¯1⊖¨⊂⍵),1 ¯1⌽¨⊂⍵ ⍝ orientations of 1st-order neighbours
gb←⍵ boundary q1 ⍝ boundary energy
t←(∨⌿↑(⊂⍵)≠¨q1)∧GA≤gt+gb ⍝ cells that will transform
gb1←q1 boundary¨⊂q1 ⍝ boundary energy when transforming into each neighbour
gb1←gb1+boundary2 q1 ⍝ add contribution of 2nd-order neighbours
gb1←gb1×1+RP×?≠⍨q1 ⍝ apply random perturbation
m←⊃⍤1⍋⍤1⍉↑gb1 ⍝ index of neighbour for minimum energy
p←⍉m⌷⍤0 1⍉↑q1 ⍝ product orientation for all cells
((,t)/,p)@(t⍨)⍵ ⍝ return new orientations
}
area←{ ⍝ ⍵: orientations
0=⊃⍵:+/0≠,⍵ ⍝ return non-zero cells for circle problem
w←(≢,⍵)÷1⌈+/,⍵≠1⌽⍵ ⍝ average grain width
h←(≢,⍵)÷1⌈+/,⍵≠1⊖⍵ ⍝ average grain height
w×h ⍝ return average grain area
}
next←{(q a)←⍵ ⋄ n←⍺ step q ⋄ n(a,area n)} ⍝ ⍺: temperature, ⍵: orientations and list of areas
⍝ return new orientations and updated list of areas
⍝ solve:
(q a)←⍺(next⍣⍵⍵)⍵(area ⍵) ⍝ get final orientations and list of areas
q(2×(a÷○1)*÷2) ⍝ return final orientations and list of diameters
}

## Slide 62: APL Grain Growth Model
gg←{
area←{0=⊃⍵:+/0≠,⍵ ⋄ (⍳2)×.((≢,⍵){⍺⍺÷1⌈+/,⍵≠1⌽[⍺]⍵})⊂⍵}
boundary←(⌈/,⍵){+⌿G0×s×1-⍟@(0∘<)s←1○○|↑(⍵-⊂⍺)÷2×⍺⍺}
step←{gt←-R×⍺×⍟?≠⍨⍵ ⋄ gb←⍵ boundary⊢q1←1 ¯1(⊖¨,⌽¨)⊂⍵ ⋄ t←(⊃(⊂⍵)∨.≠q1)∧GA≤gt+gb
gb1←(1+RP×?≠⍨q1)×{⍵+SF×q1 boundary¨⊂1 ¯1(⊖¨∘(2↓⊢),⌽¨∘(2↓⌽))q1}⍣(SF>0)boundary¨∘⊂⍨q1
m←⊃∘⍋⍤1⍉↑gb1 ⋄ (t/⍥,⍉m⌷⍤0 1⍉↑q1)@(t⍨)⍵}
R←8.314 ⋄ (GA G0 SF RP)←⍺⍺ ⋄ ⊃{⍺(2×(⍵÷○1)*÷2)}/⍺{q((⊃⌽⍵),area⊢q←⍺ step⊃⍵)}⍣⍵⍵⊢⍵(area ⍵)
}

## Slide 63: Py’N’APL Grain Growth Model
from pynapl import APL
apl = APL.APL() # APL session
gg = apl.op('''{
area←{0=⊃⍵:+/0≠,⍵ ⋄ (⍳2)×.((≢,⍵){⍺⍺÷1⌈+/,⍵≠1⌽[⍺]⍵})⊂⍵}
boundary←(⌈/,⍵){+⌿G0×s×1-⍟@(0∘<)s←1○○|↑(⍵-⊂⍺)÷2×⍺⍺}
step←{gt←-R×⍺×⍟?≠⍨⍵ ⋄ gb←⍵ boundary⊢q1←1 ¯1(⊖¨,⌽¨)⊂⍵ ⋄ t←(⊃(⊂⍵)∨.≠q1)∧GA≤gt+gb
gb1←(1+RP×?≠⍨q1)×{⍵+SF×q1 boundary¨⊂1 ¯1(⊖¨∘(2↓⊢),⌽¨∘(2↓⌽))q1}⍣(SF>0)boundary¨∘⊂⍨q1
m←⊃∘⍋⍤1⍉↑gb1 ⋄ (t/⍥,⍉m⌷⍤0 1⍉↑q1)@(t⍨)⍵}
R←8.314 ⋄ (GA G0 SF RP)←⍺⍺ ⋄ ⊃{⍺(2×(⍵÷○1)*÷2)}/⍺{q((⊃⌽⍵),area⊢q←⍺ step⊃⍵)}⍣⍵⍵⊢⍵(area ⍵)
}''')
def solve_apl(q, T, n=0):
return gg((GA, G0, SF, RP), apl.fn('≡⍥⊃') if n == 0 else n)(T, q)

## Slide 64: Benchmarks

## Slide 65: Benchmarks
Circle problem (radious 25, random perturbation, 2nd order)

## Slide 66: Benchmarks
Python 11.506s
NumPy 0.214s
APL 0.160s
Circle problem (radious 25, random perturbation, 2nd order)

## Slide 67: Benchmarks
Python 11.506s
NumPy 0.214s
APL 0.160s
Circle problem (radious 25, random perturbation, 2nd order)
The APL version runs faster in the interpreter, and it could be faster
The NumPy version could be faster too

## Slide 68: Going further
Crystallographic orientations
Growth velocity (boundary mobility)
Influence of 2nd order neighbours in formation of new boundaries
Traka, Konstantina, Karo Sedighiani, Cornelis Bos, Jesus Galan Lopez, Katja Angenendt, Dierk Raabe, and Jilt Sietsma. "Topological aspects responsible for recrystallization evolution in an IF-steel sheet–Investigation with cellular-automaton simulations." Computational Materials Science 198 (2021): 110643.

## Slide 69: Conclusions
Array programming offers clear advantages in code clarity, size and performance
The availability of intermediate results is an often-overlooked advantage
Python is a widely known, easy to learn, nice little language, but NumPy is another story
APL can be a serious contender

## Slide 70: What APL does great
Powerful array programming with a few primitives
Easy (and fast) to develop, once you learn
High performance “out of the box”
Dyalog (IDE, documentation, support)
Community

## Slide 71: Room for improvement
Unknown in some circles
Introduction for domain experts
Specialized “libraries”
Community and ecosystem

## Slide 72: To sum up

## Slide 73: To sum up
APL is great

## Slide 74: To sum up
APL is great
We need:

## Slide 75: To sum up
APL is great
We need:
  More people

## Slide 76: To sum up
APL is great
We need:
  More people
  More code

## Slide 77: Thank you

## Slide 78: Grain Growth and Array Programming
jgl@dyalog.com
jesus.galanlopez@ugent.be